## Slide 1: FIR Digital Filter Design
Aldebaro Klautau
Federal University of Para (UFPA), Belém, Brazil
Sensors and Embedded Systems Laboratory (LASSE)
Source code at https://github.com/aldebaro/dsp-telecom-book-code

## Slide 2: Finite impulse response (FIR) filter
Distinguish two properties of a filter
  Recursive or non-recursive
  Impulse response with infinite or finite duration
It is possible to have a recursive filter with a finite impulse response (e.g., when a pole cancels with a zero). Hence, FIR is not sinonymous of non-recursive but in practice a FIR filter is non-recursive
Poles of a FIR filter are located in z=0 or infinite (while an IIR filter has finite poles without this restriction). Examples:

## Slide 3: The coefficients of a FIR coincide with its impulse response
This may be very confusing! Say that Bz is an array in Octave/Matlab that represents the system function H(z) numerator while hn is an array that represents an impulse response. For a FIR, Bz and hn can be used interchangeably
For example: functions that have system functions H(z) as input parameter can be called using the “impulse response” array hn
  freqz(hn) or freqz(hn,1) will give the DTFT of hn
  y = filter(hn,1,x) will provide the ouput y to an input x through filter H(z) = Bz, which is equivalent to y=conv(hn,x) but filter eliminates the convolution tail, such that y has the same length of x

## Slide 4: Algorithms for FIR filter design
Instead of using pre-defined functions such as Butterworth's, a FIR design is typically done with alternative methods, which seek to optimize a given criterion
The most common algorithm is the least-squares (firls in Matlab/Octave
Another algorithm is Parks-McClellan’s (firpm in Matlab, not available in Octave 3.2.3)
Windowing: fir1
Arbitrary frequency response magnitude: fir2

## Slide 5: Arbitrary filter magnitude specification
An arbitrary function will be specified in NB bands of interest. For each band b, four parameters are necessary: the start fbs and end fbe frequencies, the desired function values (the magnitude in this context) Abs and end Abe at the start and end frequencies. An optional parameter is the weight of each band (e.g., W1 and W2). The larger the weight, the higher the importance given to that band

## Slide 6: Example: FIR design via least-squares

## Slide 7: Another firls example
Second band prioritized
First band prioritized

## Slide 8: FIR design via windowing
Ideal highpass
Ideal lowpass

## Slide 9: FIR design via windowing

## Slide 10: Windows

## Slide 11: FIR design via windowing
Some window desired features:
Small main lobe width  small transition band
Low amplitude of its sidelobes  stronger attenuation at rejection band

## Slide 12: Main features of a window
width of its main lobe,
amplitude of its sidelobes,
rate of sidelobe decay as frequency increases,
and scallopping loss.

## Slide 13: Window-based FIR design

## Slide 14: FIR design via windowing

## Slide 15: Two important characteristics of FIRs
FIRs are always stable
  practical FIRs have all M+1 coefficients with finite values. Hence, they are stable in BIBO (bounded input, bounded output) sense
FIRs can have linear phase
  It can be proved that the linear phase achieved if and only if there is symmetry in h[n] about some value ns.
h[n]
freqz(h)

## Slide 16: Why linear phase is important?
Recall group delay:
For a linear phase system (or filter), the group delay is constant: all frequency components delayed by this constant tg(w) = tg and signal is not distorted but simply delayed by tg samples
Nonlinear phase
Linear phase

## Slide 17: Mathematical relation between “symmetry” and “linear phase”
Example:
In general, a linear phase system can be decomposed as
where A(W) is a real function
Importance of
symmetry

## Slide 18: Four types of symmetric FIR filters

## Slide 19: Impulse and frequency responses for the four types of symmetric FIR filters
Zeros close to the unit circle may impact phase linearity