## Slide 1
Aldebaro Klautau – www.laps.ufpa.br
Belém, Brazil – October 13, 2015
Federal University of Para (UFPA)
Multicarrier Modulation
DMT / OFDM

## Slide 2: Multicarrier Modulation
What is the essence and motivation?
Partition the communication channel into several small “subchannels”
sub-carrier
|H(f)|

## Slide 3: Multicarrier Modulation
The information at each “subchannel” is located in frequency by a “tone”, also called “bin” and “sub-carrier” (avoid calling “carrier”)
Example: DSL uses 4.3125 kHz as “tone spacing”
sub-carrier

## Slide 4: Multicarrier Modulation
Discrete Multitone (DMT) ≈ Orthogonal Frequency-Division Multiplexing (OFDM)‏
OFDM is a “passband” modulation
  Overall spectrum is centered at a carrier frequency (e.g. 2.4 GHz). It is adopted for wireless communications
  Similar to a QAM, the OFDM signal (before frequency upconversion) is complex-valued
DMT is a “baseband” modulation
  Overall spectrum is centered at DC (0 Hertz). It is adopted in DSL technologies (ADSL, VDSL, etc.)
  Similar to a PAM, the signal is real-valued

## Slide 5: WiFi: Example of OFDM Spectrum
Notes: From https://www.fcc.gov/help/public-safety-tech-topic-10-license-exempt-wireless-applications-public-safety

## Slide 6: ADSL2+: Example of DMT Spectrum
POTS: Plain Old Telephony Service
Upstream: Transmission from customer to central office
Downstream: Transmission from central office to customer
Notes: From https://www.fcc.gov/help/public-safety-tech-topic-10-license-exempt-wireless-applications-public-safety

## Slide 7: Signal Attenuation
Notes: From http://www.atnf.csiro.au/people/atzioumi/jdsu/xDSL%20Overview%20Oct%2008.ppt

## Slide 8: Bits per tone

## Slide 9: DSL Standards
Family | ITU | Name | Ratified | Maximum Speed capabilities
ADSL | G.992.1 | G.dmt | 1999 | 8 Mbps down 800 kbps up
ADSL2 | G.992.3 | G.dmt.bis | 2002 | 8 Mb/s down 1 Mbps up
ADSL2plus | G.992.5 | ADSL2plus | 2003 | 24 Mbps down (Amend 1, 29Mbps) 1 Mbps up
ADSL2-RE | G.992.3 | Reach Extended | 2003 | 8 Mbps down 1 Mbps up
VDSL | G.993.1 | Very-high-data-rate DSL | 2004 | 55 Mbps down 15 Mbps up
VDSL1 -12 MHz long reach | G.993.2 | Very-high-data-rate DSL 2 | 2005 | 55 Mbps down 30 Mbps up
VDSL2 - 30 MHz Short reach | G.993.2 | Very-high-data-rate DSL 2 | 2005 | 100 Mbps up/down
Slide from JDSU

## Slide 10: DSL Frequency Ranges & Rates
25kHz 1.1MHz 2.2MHz 12MHz Frequency 30MHz
ADSL2+
ADSL
VDSL
VDSL2
Technology | Freq range | Max Rates | Max # of sub-carriers and Bin spacing
ADSL | 25kHz – 1.1MHz | 800kbps up 8Mbps down | 256 with 4.3125kHz bins
ADSL2+ | 25kHz – 2.2MHz | 1Mbps up 24Mbps down | 512 with 4.3125kHz bins Amend. 1 = 29 Mbps down
VDSL(1) | 25kHz – 12MHz | 15Mbps up 55Mbps down | 2782 with 4.3125kHz bins
VDSL2 | 25khz – 30MHz | 100Mbps up 100Mbps down | 4096 with 4.3125kHz bins 3478 with 8.625kHz bins
Technology
17.66MHz
Slide from JDSU

## Slide 11: DMT
Hereafter we will emphasize DMT
The DMT bitloading is based on a “waterfilling” algorithm
We are not going to discuss the theory, but the idea of waterfilling is that more bits are loaded in tones with higher SNR values
Next slides indicate how DMT works

## Slide 12: Typical DMT (baseband) System
DMT / OFDM  use Fast Fourier Transform (FFT) for modulation

## Slide 13: Slice the bitstream according to bitloading table
input bitstream: 010100011010110100001...
k-th frame 01
010001
1010
1110
4
4
4
3
6
2
2
1
# bits
Tone
Bitloading
input bitstream: 01-010001-1010-1101-0...

## Slide 14: Mapping: from bits to symbols
QAM symbols: 1+j8 4-j4 3+j3 1+j2
01
010001
1010
1110

## Slide 15: Inverse FFT
Use 8-points FFT for this example
Need Hermitian symmetry to get real signal
X = [1 4-j4 3+j3 1+j2 8 1-j2 3-j3 4+j4]
x = ifft(X)‏
x = [25.0 -5.9 15.0 -2.4 5.0 -20.1 -9.0 0.4]
QAM symbols: X(0)=1, X(4)=8 X(1)=4-j4 X(2)=3+j3 X(3)=1+j2
Add cyclic-prefix (example: CP with 3 samples)‏
x=[-20.1 -9.0 0.4 25.0 -5.9 15.0 -2.4 5.0 -20.1 -9.0 0.4]

## Slide 16: Inverse FFT and add CP
Use 8-points FFT for this example
Need Hermitian symmetry to get real signal
X = [1 4-j4 3+j3 1+j2 8 1-j2 3-j3 4+j4]
x = ifft(X)‏
x = [25.0 -5.9 15.0 -2.4 5.0 -20.1 -9.0 0.4]
QAM symbols: X(0)=1, X(4)=8 X(1)=4-j4 X(2)=3+j3 X(3)=1+j2
Add cyclic-prefix (example: CP with 3 samples)‏
x=[-20.1 -9.0 0.4 25.0 -5.9 15.0 -2.4 5.0 -20.1 -9.0 0.4]

## Slide 17: Typical DMT-based DSL System
Samples
Symbols
QAM symbols: X(0)=1, X(4)=8 X(1)=4-j4 X(2)=3+j3 X(3)=1+j2

## Slide 18: Fundamental DMT Equation
Yk = Xk Hk
Hk pode ser obtido da DTFT (discrete-time Fourier transform) da resposta ao impulso h[n] do canal na frequência correspondente
sub-carrier

## Slide 19: Vectors of interest in DMT simulation
Samples
Symbols

## Slide 20: Vectors of interest in DMT simulation
Alternative view:

## Slide 21: Simple DMT transmission example in Matlab

## Slide 22: Step-by-step debugging of DMT in Matlab