## Slide 1: Maximum Likelihood (ML) and Maximum a Posteriori (MAP) Decision Criteria
Aldebaro Klautau
LASSE - Federal University of Pará (UFPA)
Brazil, Jun. 02, 2017

## Slide 2: Agenda
What is “likelihood”?
  Histogram of signal samples
Bayes’ rule: likelihood, prior, posterior and evidence
iid
MLE
  Examples
Decision criteria for classifiers and digital communication receivers
  ML
  MAP

## Slide 3: Histogram
Example: random signal (x=randn(1,100) using Matlab/Octave)
Time-domain waveform
plot(x) on Matlab/Octave
Histogram with 10 bins :
hist(x) on Matlab/Octave

## Slide 4: Estimation of PMF or PDF via normalized histograms
Normalizing the histogram by the total number of samples provides an estimate of the probability mass function (PMF). When this result is further normalized by the bin width, an estimate of the probability density function (PDF) is obtained.
[n,a]=hist(x)
bar(a,n/length(x),'hist')
[n,a]=hist(x)
bar(a,n/length(x) / ...
(a(2)-a(1)),'hist')

## Slide 5: Likelihood
Likelihood is the actual value of a probability density function (PDF). It is not a probability and can be larger than 1. Superimposed PDFs and their estimation
Gaussian with mean = 4 and variance = 0.09 104 examples
Standard Gaussian with mean = 0 and variance = 1
100 examples

## Slide 6: Bayes’ rule
Based on the definition of conditional probability
P(A,B) = P(B,A) = P(B) P(A/B) = P(A) P(B/A)
Hence: P(B/A) = [P(B) P(A/B)] / P(A)
Used in many applications:
  Digital communications: A is the received bit and B the hypothesized transmitted bit
  Classification: A is the set of features and B the class
Note: “A” can be a continuous random variable (rv) while “B” is a discrete rv. In this case, P(A) and P(A/B) are likelihoods of two distinct PDFs, while P(B) and P(B/A) are distinct PMFs

## Slide 7: Bayes’ theorem (in the context of classification)
To apply Bayes’ theorem, typically one needs to estimate likelihoods and priors for each class:
http://shatterline.com/blog/2013/09/12/not-so-naive-classification-with-the-naive-bayes-classifier/
classifier
x1
Class
x2
xN
...
input features

## Slide 8: Example of Bayes classifier
Assume 4 classes and that each likelihood is a Gaussian distribution (dictated by “nature”)
Also assume the priors are uniformly distributed P(Classj)=1/4
Given a test vector x, calculate posteriors for j=1, 2, 3, 4 and choose the largest:
If the estimation of likelihoods and priors is perfect, the Bayes classifier is optimum and its error is the minimum possible, called “Bayes error”

## Slide 9: Naïve Bayes classifier
Use the naïve (ingenuous) assumption that the parameters of each class are statistically independent, such that all joint distributions are equivalent to the multiplication of the marginal distributions
  Example, for a parameter vector z = [x, y] of a classe C, it corresponds to P(z|C) = P(x|C) P(y|C)

## Slide 10: Naïve classifier using Gaussians for real-valued features
For each class, estimate the needed statistics, priors and likelihoods
Class 0:
  prior0=4/7
  m0l=mean([12 14 14 13.8]) %13.450
  m0w=mean([3.2 2.8 2.4 1.5]) %2.4750
  s0l=std([12 14 14 13.8]) %0.97125
  s0w=std([3.2 2.8 2.4 1.5]) %0.72744
Class 1:
  prior1=3/7
  m1l=mean([10 13 11]) %11.333
  m1w=mean([0.5 1.8 1]) %1.1000
  s1l=std([10 13 11]) %1.5275
  s1w=std([0.5 1.8 1]) %0.65574
Test example: x=[13 3.2]; xl=x(1); xw=x(2);
  num0=normpdf(xl,m0l,s0l)*normpdf(xw,m0w,s0w)*prior0
  num1=normpdf(xl,m1l,s1l)*normpdf(xw,m1w,s1w)*prior1
  Px=num0+num1; %denominator, just a scale factor
  posterior0=num0/Px %0.99685
  posterior1=num1/Px %0.0031541

## Slide 11: iid: independent and identically distributed
When a random vector X=[x1, x2, ..., xN] is composed by statistically independente random variables (rv), the likelihood P(X) can be conveniently decomposed as
  P(X) = P1(x1) P2(x2) ... PN(xN)
If, besides independen, the rv’s are obtained from the same distribution, i. e., all distributions P1(.), P2(.), ..., PN(.) are identical, then the rv’s are iid
When maximizing (or minimizing) P(X), it is convenient to use log P(X) instead because it allows the use of summations instead of products
  The log is monotonic, so the arguments / parameters that maximize P(X) are the same ones that maximize log P(X)
  We then often decide based on the log-likelihood function

## Slide 12: Maximum likelihood estimation (MLE)
Several applications require “parameter estimation”
  There are many methods (least-squares, MLE, etc.)
MLE: aims at finding the parameters that maximize a given likelihood of a given data. It is cast in a probabilistic framework
  In telecom we want to find the transmitted bits (ML decoding) not model parameters but it has strong similarities with MLE
Examples of MLE:
  MLE of a Bernoulli B(p) random variable (coin flips, p is the probability of “head”). Given N flips of the coin, the MLE of p is p= H / N, where H is the “number of heads” in the N flips.
  MLE for univariate Gaussian mean of X1, X2, ..., Xn is the sample average:
For proofs of the two examples, see e.g. https://onlinecourses.science.psu.edu/stat414/node/191

## Slide 13: Memoryless channels
AWGN, BSC and other memoryless channels simplify the math because the output at instant t depends only on the input at t
Assume the output of a memoryless channel is the sequence Y=y1, y2 when the input is X=x1, x2, the probability P(Y/X) can be written as
  P(Y/X) = P(y1 / x1) P(y2 / x2) because the channel is memoryless
  Note that P(Y) = P(y1) P(y2) ... P(yN) requires yi to be iid, but the equation P(Y/X) = P(y1 / x1) P(y2 / x2) is valid even if yi are not independent, because given xi and a memoryless channel, yi does not depend on inputs and outputs at “time” different than i
Example, assume Z and U(m) are the output and input sequences of a BSC, being composed by words Zi and Ui(m), respectively, each with n bits zji and uji(m). The superscript m indicates the codeword U depends on information bits m. The convolutional code output U is not formed by iid codewords (hence, Z is not formed by iid words). In spite of not being iid, because the channel is memoryless, ML sequence decoding can use:

## Slide 14: Two decision criteria for sequence detection
Maximum likelihood (ML): max P(Z / U)
Maximum a posteriori (MAP): max P(U / Z)
Information
source
Rate 1/n
Conv. encoder
Modulator
Information
sink
Rate 1/n
Conv. decoder
Demodulator
Channel

## Slide 15: Decision criteria
In block coding there is a deterministic bijective mapping between the message m and its codeword U(m) (or simply U) such that finding the codeword U allows to find m
In convolutional coding, the codeword U(m) (or simply U) depends on the input and previous L input values (the current “state”). Hence, decoding is equivalent to finding the best state sequence over the trellis given the received symbols Z, which then enables estimating (uncovering) the hidden information m
Best path according to maximum likelihood (ML): maxU P(Z / U)
  Recall that hypothesizing all codewords U (or U(m)) requires trying all messages m
  Likelihoods are often easier to calculate than posterior probabilities
Best path according to maximum a posteriori (MAP): maxU P(U / Z) = maxU P(Z / U) P(U)
  The MAP criterion takes in account not only the likelihood but also the prior
  Achieves the minimum probability of error (it is the optimum criterion)
ML and MAP lead to the same decision when all sequences U have the same probability, that is P(U) is a constant or “the prior is uniform”

## Slide 16: Symbol-by-symbol versus sequence decisions
Given a sequence of received symbols Z, in general, the optimum decision needs to take in account the whole sequence but when the symbols are independent, a symbol-by-symbol decision (SbS) leads to the same (optimum) result and is often much simpler
  In other words: we need to use sequence decision when the symbols are related, which happens at: 1) the transmitter (by a convolutional code, for example) , 2) the channel (by a LTI system with memory) and 3) both
Viterbi is an algorithm for ML sequence decision (MLSD) and can be used in any trellis: it finds the “best path” in ML sense over the trellis. It is often used in digital communications for:
  convolutional decoding (case 1 above) and
  combating intersymbol interference (ISI) caused by the signal dispersion in channels with memory (case 2 above)

## Slide 17: General Viterbi setup
Many practical applications:
convolutional decoding and channel trellis decoding
fading communication channels
partial response channels in recording systems
optical character recognition
speech recognition
DNA sequence analysis
Find a path through any Markov graph, which is a sequence of states governed by a Markov chain
What is the best estimate for the information given the observation?
noise
information
Finite State Machine
observation
x
n
y = x + n

## Slide 18: Sequence decision for convolutional decoding over memoryless channel
Has “memory”, creates “structure”
Sequence decision,
exploits the “structure”
Memoryless

## Slide 19: Sequence decision for uncoded information over channel with memory
Has “memory”, for
example with impulse response h(t) = d(t) + 0.5 d(t-3) It creates “structure”
Memoryless
Sequence decision,
exploits the “structure”

## Slide 20: Distinguish: symbol-by-symbol, block-based and sequence decision
Make sure you distinguish the three cases. We assume (literature may use different definitions):
In symbol-by-symbol decision, the decoder operates on a single number
In block-based decision, the decoder operates on a block of N symbols and the blocks are statistically independent of each other
  For example, the decision is made on the output of a memoryless channel whose input are the codewords of a block code (n, k). There is a sequence of N = n bits in this case, but the endpoints of the block limit the influence of a given symbol (it does not influence the next block)
In sequence decision, there is a continuous flow of symbols passing by a system with memory such that a symbol influences the following L, assuming a finite memory of L symbols
  The L-symbols memory defines the states of a trellis that impose “structure” and the search can benefit from this structure
  This is the situation that can be tackled with the Viterbi and similar MLSD algorithms

## Slide 21: Block-based and sequence decision similarities
To restrict latency to reasonable values, convolutional decoding adopts truncation of a bitstream into “packets” and becomes more similar to block-based decoding
In fact, MLSD (Viterbi, etc.) can be used to decode block codes
  See, e.g., [Lathi & Ding, 2010, 4th Ed.], Section 14.7 “Trellis diagram of block codes”
  Makes more sense when the block is relatively large

## Slide 22: Block-based decision for repetition code
Repeat each bit 3 times
1
0
1
0
1
111
000
111
000
111
Input bits
Coded (channel input) bits U
101
110
110
100
111
Channel output bits
Easier to make decisions for each three bits
No need for finding the best path over a trellis: the input bit is easily obtained from the estimated codeword

## Slide 23: MLSD: Brute force versus Viterbi algorithm
For the example code:
1
0
1
0
0
11
10
00
10
11
Input bits m
Coded (channel input) bits U
Tail bits
11
11
10
10
11
Channel output bits Z
Number of possible sequences (two equivalent reasoning):
  5 among the 4 possible codewords: 45 = 1024 or sequences of 10 bits: 210 = 1024
Brute force:
  Enumerate all 1024 candidates Ui and calculate the likelihood P(Z / Ui)
  After choosing the best sequence of codewords U*, still needs to find the corresponding input m. Some codeword sequences may not be allowed
When Viterbi finds the best path, it helps in two aspects:
  It saves computation and already informs the estimated input m taking in account all restrictions (“structure”) in the generation of U

## Slide 24: Example of brute force
For the example code:
11
11
10
10
11
Channel output bits Z
List (hypothesize) all possibilities:
00
00
00
00
00
00
00
00
00
01
00
00
00
00
10
00
00
00
00
11
00
00
00
01
00
00
00
00
01
01
11
11
11
11
11
.
.
.

## Slide 25: Dynamic programming
Viterbi is a “dynamic programming” algorithm
Find the quickest way from London to Vienna. The labels on each path are travel times (from [Sklar]).

## Slide 26: Viterbi / dynamic programming example
Collect metric and backtrace information
Best path, from last state to first: Vienna  Munich  Paris  London
Best path total time: 26

## Slide 27: Thanks!
Contact: lasse@ufpa.br
www.lasse.ufpa.br